## Slide 1: Explosion Effects
Joseph E Shepherd
California Institute of Technology
Pasadena, CA USA 91125
Joseph.E.Shepherd@caltech.edu
Presented at
The Fourth European Summer School on Hydrogen Safety
Coralia Marina Viva, Corsica, France
7th – 16th September 2009,
TexPoint fonts used in EMF.
Read the TexPoint manual before you delete this box.: AAAAAAA

## Slide 2: Topics
Introduction
Ideal Blast Waves
Mechanics and Strength of Materials
Modes of Structural Response
Modeling Structural Response
Blast Loading Dynamic Reponse – Cantilever Beam
Internal Explosions – Deflagrations and Detonations
References

## Slide 3: Introduction
Explosions create high-pressure, high-temperature gases that can cause:
Mechanical failure due to pressure or blast waves or internal pressure build-up.
  Permanent deformation or equipment or structures
  Rupture or tearing of metal or building components
  Creating flying fragments or missiles
  Blast, fragment or impact injury
Thermal failure due to heat transfer from fireball or hot combustion products.
  Softening of metal structures
  Ignition of building materials, electrical insulation, plastic or paper products
  Burn injuries to skin and eyes
Combination of fire and explosion, thermal and mechanical effects often occur.

## Slide 4: Mechanical effects from high pressure
Expansion of combustion products due to conversion of chemical to thermal energy in combustion and creation of gaseous products in high explosives
Expansion ratio for gaseous explosions depends on thermodynamics
Expansion rate depends on chemical kinetics and fluid mechanics
  Flame speeds
  Detonation velocity

## Slide 5: Thermal effects from high temperature
Hot gases radiate strongly in IR, particularly for sooting explosion like BLEVE.
  Fireballs cause injury (skin burns) and secondary ignition of structures
Internal explosions create high-speed gas and convective heat transfer in addition to IR radiation
  Heat up equipment, ignite flammable materials

## Slide 6: Fragment effects from structural failure
Primary fragments
  Created by rupture of vessel or structure
  Some fraction of explosion energy transferred to fragment
  Follows a ballistic trajectory
Secondary fragments
  Created by blast wave and following flow
  Accelerated by flow, eventually follows a ballistic trajectory
Both lift and drag important in determining trajectories

## Slide 7
Pasadena TX 1989 – C2H4
Flixborough 1974 - cyclohexane
Port Hudson 1974 – C3H8
(20 Kg H2 )
Notes: H2 explosion photo (could be Porsgrunn Norway 6 July 1985 ammonia plant or possibly Sarnia Ontario 1984) is from Dag Bjerketvedt’s web site, same photo is also on Gexcon site, the rest are from AIChE 1994 guidelines book.

## Slide 8: Pasadena TX 1989
Notes: From USFA Report 035, Major Fires Investigation Project, Phillips Petroleum Chemical Plant Explosion and Fire October 23, 1989

## Slide 9: Nuclear Blast Wave Damage – 5 psi (34 kPa)
Notes: From Glasstone – Effects of Nuclear Weapons 1977

## Slide 10: Effects of High Explosive Detonation

## Slide 11: Truck Bomb – 4000 lb TNTe

## Slide 12: Response of a Large Structure is Complex!
Blast effects cause a small number of columns and slabs to directly fail
Increased load on other structural elements leads to progressive collapse
In Murrah Building, 40% of floor area destroyed due to progressive collapse, only 4% due to direct blast.
Factors in progressive collapse
  Building design (seismic resistance can help)
  Fires can weaken structural elements (WTC)
Detailed analysis and testing is needed to understand or predict response
Notes: FEMA 227 (1995) and FEMA 439a (2005) reports on building performance. NIST and ASCE studies on WTC.

## Slide 13: Preview – Structural Response Analysis
First, estimate static capacity of structure. Failure can occur to do either
  Excessive stress – plastic deformation or fracture makes structure too weak for service
  Excessive deformation – structure not useable due to leaks in fittings or misfit of components (rotating shafts, etc).
Second, what are structural response times?
    Large spectrum for a complex structure
    Single value for simple structure
  How do these compare to loading and unloading times of pressure wave?
    Loading time
    Unloading time
Third, estimate dynamic peak deflection and stresses based on response times and loading history
  High peak load is acceptable if duration is short (impulsive case)
  Lower peak load limit if duration is long and rapidly applied (sudden case)

## Slide 14: Structural Response
Structures move in response to forces (Newton’s Law)
  Structure has mass and stiffness
  Structure “pushes back”

## Slide 15: Determining structural loads
Load generally means “applied force” in this context. The primary load is usually thought of as due to pressure differences created by the explosion process. Pressure differences across components of a structure create forces on the structure and internal stresses.
Three simple cases
  External explosion
  Blast wave interaction
  Internal explosion

## Slide 16: External Explosion
Explosion due to accidental vapor cloud release and ignition source starting a combustion wave
Flame accelerates due to instabilities and turbulence due to flow over facility structures
Volume displacement of combustion (“source of volume”) compresses gas and creates motion locally and at a distance
  Blast wave propagates away from source
Unconfined Vapor Cloud Explosion (UVCE)

## Slide 17: Blast Wave Interaction
Blast wave consists of
  Leading shock front
  Flow behind front
Pressure loading
  Incident and reflected pressure behind shock
  Stagnation pressure from flow
Factors in loading
  Blast decay time
  Diffraction time
  Distance from blast origin

## Slide 18: Internal Explosion
Can be deflagration or detonation
Deflagration
  Pressure independent of position, slow
Detonation
  Spatial dependence of pressure
  Local peak associated with detonation wave formation and propagation

## Slide 19: Loading Histories
Pressure-time histories can be derived from several sources
  Experimental measurements
  Analytical models with thermodynamic computation of parameters
  Detailed numerical simulations using computation fluid dynamics
  Empirical correlations of data
  Approximate numerical models of blast wave propagation (Blast-X)
Characterizing pressure-time histories
  Single peak or multiple peaks
  Rise time
  Peak pressure
  Duration
Slow flame in vessel
High speed flame in vessel
Nonideal explosion
Ideal blast wave

## Slide 20: Ideal Blast Waves

## Slide 21: Formation of a Shock Wave

## Slide 22: Characteristics of Shock Waves
Supersonic compression wave
Very thin (0.1 um for NTP)
Common examples:
  Sonic booms
  Blast waves from explosions
  Leading shock in detonation
Described by Rankine-Hugoniot relations
Piston model
Ushock
upiston
1
2

## Slide 23: Rankine-Hugoniot Relations
Combine conservation of mass, momentum, and energy across the wave front
Rankine-Hugoniot Eqn H
Rayleigh Eqn R

## Slide 24: Blast Wave
shock

## Slide 25: Detonation

## Slide 26: Ideal Blast Wave Sources
Simplest form of pressure loading – due concentrated, rapid release of energy
High explosive or “prompt” gaseous detonation. Main shock wave followed by
pressure wave and gas motion, possibly secondary waves.
Inside Explosion
Pfortner
Notes: Experiment by Pfortner at Fraunhofer Institute.

## Slide 27: Interaction of Blast Waves with Structures
Blast-wave interactions with multiple structures LHJ Absil, AC van den Berg, J. Weerheijm p. 685 - 290,
Shock Waves, Vol. 1, Ed. Sturtevant, Hornung, Shepherd, World Scientific, 1996.

## Slide 28: Idealized Interactions
Enhancement depends:
Incident wave strength
Angle of incidence
“Explosions in Air” Baker
Notes: Plot is from “Explosions in Air” Baker p. 6-14.

## Slide 29: Blast and Shock Waves
Leading shock front pressure jump determined by wave speed – shock Mach number.
Gas is set into motion by shock then returns to rest
Wave decays with distance
Loading determined by
  Peak pressure rise
  Impulse
  Positive and negative phase durations
Specific impulse!
Notes: See Baker et al.

## Slide 30: Scaling Ideal Blast Waves I.
Dimensional analysis (Hopkinson 1915, Sachs 1944, Taylor-Sedov)
  Total energy release E = Mq
    M = mass of explosive atmosphere (kg)
    q = specific heat of combustion (J/kg)
  Initial state of atmosphere Po or o and co
Limiting cases
  Strength of shock wave
    Strong  P >> Po
    Weak  P << Po
  Distance from source
    Near R ~ Rsource
    Far R >> Rsource

## Slide 31: Scaling Ideal Blast Waves II.
Scale parameters
  Blast length scale Rs = (E/Po)1/3
  Time scale Ts = Rs/co
  Pressure scale
    Close to explosion Pexp (usually bounded by PCJ)
    Far from explosion Po
Nondimensional variables
  pressure  P/Po
  distance R/Rs
  time t/Ts
  Impulse (specific) I/(Po Ts)
Relationships:
DP = Po F(R/Rs)
I = Po Ts G(R/Rs)

## Slide 32: Cube Root Scaling in Standard atmosphere
Simplest expression of scaling (Hopkinson)
  At a given scaled range R/M1/3, you will have the same scaled impulse I/M1/3 and overpressure  P
  When you increase the charge size by K, overpressure will remain constant at a distance KR, and the duration and arrival time will increase by K.
Notes: See Baker “Explosions in Air” AMCP 706-181

## Slide 33: TNT Equivalent
Ideal blast wave from gaseous explosion equivalent to that from High Explosive (TNT) when energy of gaseous explosive is correctly chosen
Universal blast wave curves in far field when expressed in Sachs’ scaled variables
For ideal gas explosions (detonations) E is some fixed fraction of the heat of combustion (Q = qM)
For nonideal gas explosions (unconfined vapor clouds), E is quite a bit smaller. Key issues:
  How to correctly select energy equivalence?
  How to correctly treat near field?
Notes: See Dorofeev AIChE paper 2006.

## Slide 34: Energy Equivalent for Common Explosives
Explosive | Q (MJ/kg) | Density (g/cc) | CJ velocity (km/s) | CJ Pressure (kbar)
TNT | 4.52 | 1.6 | 6.7 | 210
RDX | 5.36 | 1.65 | 8.7 | 340
HMX | 5.68 | 1.9 | 9.1 | 390
Tetryl | 4.52 | 1.73 | 7.85 | 260
C6H14 | 45 (1.62) | 0.66 | 1.8 | 0.018
H2 | 100 (2.7*) | 8.2E-5 | 1.97 | 0.015
Values from Baker et al.
* For fuel-air mixture

## Slide 35: Blast Wave from Hydrogen-Air Detonation
Outside
explosion
Shepherd 1986
Notes: Experiments by Bill Benedick and Joe Shepherd, Sandia National Lab, Albuquerue NM 1985
The total amount of H2 was 148 g or 63.9 scf of H2 contained in a rectangular bag 181 cu ft., centerline 15' off ground, 14.8 MJ equivalent.
Nitroguanidine (NQ) comparison test was 11 lb cylinder suspended at centerline height aligned with long axis of rectangle and NQ energy equivalent used was 2.84 MJ/kg. H2-air (stoichiometric) energy equivalent was 100 MJ/kg of H2 or 2.71 MJ/kg of fuel-air mix.
"Blast Waves in Ducts", JE Shepherd, August 11-12, 1986, OECD/IGUS working group, Thun Switzerland.

## Slide 36: Scaling of Blast Pressure – Ideal Detonation
Comparison of fuel-air
bag tests to high explosives
Work done at DRES
(Suffield, CANADA) in 1980s
Moen et al 1983
Notes: From Moen et al 1983

## Slide 37: Scaling of Impulse – Ideal Detonation
Air burst
Surface burst
For the same overpressure or scaled impulse at a given distance, M(surface) = 1/2 M(air)
Moen et al 1983

## Slide 38: Energy scaling of H2-air blast
Energy Equivalence
100 MJ/kg of H2
or
2.71 MJ/kg of fuel-air mix for stoichiometric.
Shepherd 1986
Notes: Experiments by Bill Benedick and Joe Shepherd, Sandia National Lab, Albuquerue NM 1985. Continuous curves are from Baker “Explosions in Air”.
The total amount of H2 was 148 g or 63.9 scf of H2 contained in a rectangular bag 181 cu ft., centerline 15' off ground, 14.8 MJ equivalent.
Nitroguanidine (NQ) comparison test was 11 lb cylinder suspended at centerline height aligned with long axis of rectangle and NQ energy equivalent used was 2.84 MJ/kg. H2-air (stoichiometric) energy equivalent was 100 MJ/kg of H2 or 2.71 MJ/kg of fuel-air mix.
"Blast Waves in Ducts", JE Shepherd, August 11-12, 1986, OECD/IGUS working group, Thun Switzerland.

## Slide 39: Hydrogen-air Detonation in a Duct
Blast waves in ducts decay much more slowly than unconfined blasts  P ~ x-1/2
Multiple shock waves created by reverberation of transverse waves within duct
Pressure profile approaches triangular waveshape at large distances.
Thibault et al 1986
Notes: P. A. Thibault, J. D. Penrose, J. E. Shepherd, W. B. Benedick, and D. V. Ritzel 1988 ``Blast Waves Generated by Planar Detonations,'' 16th Intl. Symp. Shock Tubes and Waves, Ed. H. Grönig, VCH Publishers Inc, NY, 765-771.

## Slide 40: Nonideal Explosions
Blast pressure depends on magnitude of maximum flame speed
Flame speed is a function of
  Mixture composition
  Turbulence level
  Extent of confinement
There is no fixed energy equivalent
  E varies from 0.1 to 10% of Q
Impulse and peak pressure depend on flame speed and size of cloud – Sachs’ scaling has to be expanded to include these

## Slide 41: Pressure Waves from Fast Flames
Sachs’ scaling with addition parameter – effective flame Mach number Mf. Numerical
simulations based on ‘porous piston’ model and 1-D gas dynamics.
Tang and Baker 1999
Notes: M.J. Tang and Q.A. Baker "A New Set of Blast Curves from Vapor Cloud Explosion", Process Safety Progress, 18(3), 1999, 234-240.

## Slide 42: What is Effective Flame Speed?
Dorofeev 2006
Consider volume displacement
of a wrinkled (turbulent) flame growing in
a mean spherical fashion.
Expansion
ratio
Notes: Dorofeev 2006 AIChE Meeting, 40th Loss Prevention Seminar

## Slide 43: Mechanics and Strength of Materials

## Slide 44: Forces, Stresses and Strains
Loading becomes destructive when forces are sufficient to displace structures that are not anchored or else the forces (or thermal expansion) create stresses that exceed yield strength of the material.
Important cases
  Rigid body motion – fragments and overturning
  Deformation due to internal stresses
    Bending, beams and plates
    Membrane stresses, pressure vessels

## Slide 45: Rigid Body Forces due to Explosion
Pressure varies with position and time over surface – has to be measured or computed
Local increment of force on surface due to pressure only in high Reynolds’ number flow
Geometry and distribution of pressure will result in moments as well as forces!
Be sure to add in contributions from body forces (gravity) to get total force.
Notes: Add formulas and sketches to define force from pressures, show

## Slide 46: Consequence of Forces I.
Rigid body motions
  Translation
  Rotation
X’ = X – Xcm distance from center of mass

## Slide 47: Internal Forces Due to an Explosion
Force on a surface element dS
Stress tensor s

## Slide 48: Consequence of forces – small strains (<0.2 %)
Elastic deformation
Elastic strain
Elastic shear
Youngs’ modulus E, shear modulus E, and Poisson ratio n are material properties

## Slide 49: Consequences of forces – large strains
Onset of yielding for s ~ sY
Necking occurs in plastic regime s > sY
Plastic instability and rupture for s > su
Energy absorption by plastic deformation
Plot is in terms of engineering stress and strain, apparent
maximum in stress is due to area reduction caused by necking

## Slide 50: Stress-Strain Relationships

## Slide 51: Yield and Ultimate Strength
Yield point sYP determined by uniaxial tension test
Yielding is actually due to stress differences or shear. Extension of tension test to multi-axial loading:
  Maximum shear stress model max < YP/2
  Von Mises or octahedral shear stress criterion
Onset of localized permanent deformation occurs well before complete plastic collapse of structure occurs.
Notes: See Ugural and Fenster Chapter 4.

## Slide 52: Some Typical Material Properties

## Slide 53: Considerations about material properties
Simple models:
  perfectly plastic,
  elastic perfectly plastic
More realistic models
  Strain hardening Y ()
  Strain rate effects, Y(d/dt)
  Temperature effects Y(T)
s
e
s
e
de/dt

## Slide 54: Modes of Structural Response

## Slide 55: Mechanism of Structural Deformation
Stress waves
  Longitudinal or transverse
  Short time scale
Flexural waves
  Shock or detonation propagation inside tubes
  Vibrations in shells
tension or compression
  Deforms shells
shearing loads
  Bends beams and plates

## Slide 56: Pressure Loading Characterization
Structural response time T vs. loading and unloading time scales
Peak pressure  P vs. Capacity of structure
Loading regimes
  Slow (quasi-static), typical of flame inside vessels T << L or u
  Sudden, shock or detonation waves L << T
    Short duration – Impulsive U << T
    Long duration - Step load T << U
DP

## Slide 57: Statics vs. Dynamics
Static loading T << l, u
  Loading and unloading times long compared to characteristic structural response time
  Inertia unimportant
  Response determined completely by stiffness, magnitude of load.
Dynamic loading T ≥ l, u
  Loading or unloading time short compared to characteristic structural response time
  Inertia important
  Response depends on time history of loading

## Slide 58: Static Stresses in Spherical Shell
Balance membrane stresses with internal pressure loading
Force balance on equator
Membrane stress
Validate only for thin-wall vessels h < 0.2 R
R
R

## Slide 59: Static Stresses in Cylindrical Shells
Biaxial state of stress
Longitudinal stress due to projected force on end caps.
Radial (hoop) stress due to projected force on equator

## Slide 60: Bending of Beams
Force on beam due to integrated effects of pressure loading
Pure bending has no net longitudinal stress
Deflection for uniform loading

## Slide 61: Stress Wave propagation in Solids
Dynamic loading by impact or high explosive detonation in contact with structure
Two main types
  Longitudinal (compression, P-waves)
  Transverse (shear, S-waves
Stress-velocity relationship (for bar P-waves)
Cl exact for bar

## Slide 62: Is direct stress wave propagation important?
Time scale very fast compared to main structural response T ~ L/C
  Average out in microseconds (10-6 s)
Stress level low compared to yield stress  ~  P ~ 10 MPa << Y = 200- 500 MPa
 | Cl (m/s) | Cs(m/s)
Steel | 6100 | 3205
Aluminum | 3205 | 3155
Direct stress propagation within the structural elements is usually
not relevant for structural response to gaseous explosions. Important for high
explosive when structure is very close or in direct contact with explosive

## Slide 63: Vibration of Plates, Beams, & Structures
Element vibrations
  Membranes or shells
  Plates or beams
  Modes of flexural motion
    Standing waves, frequencies i
    Propagating dispersive waves (k)
Coupled motions of entire structure

## Slide 64: Free Vibration of Clamped Plate
Morse and Ingard Theoretical Acoustics

## Slide 65: Transient Response of Clamped Plate
Morse and Ingard
Theoretical Acoustics

## Slide 66: Modes of a Piping System

## Slide 67: Piping System Oscillation Frequencies

## Slide 68: Two Special Situations
Loading on small objects
  Represent forces as drag coefficients dependent on shape and orientation and function of flow speed.
  F = ½  V2 CD(Mach No, Reynolds No) x Frontal Area
Thermal stresses.
  Thermal stresses are stresses that are created by differential thermal expansion caused by time-dependent heat transfer from hot explosion gases. This is distinct from the loss of strength of materials due to bulk heating, which is a very important factor in fires which occur over very much longer durations than explosions.
   = /E +   T
Notes: Drag Coefficients for simple objects are discussed in Baker et al, p. 237
Thermal Stresses are discussed in the book by Nota and Chapter 13 of Timoshko and Goodier

## Slide 69: Modeling Structural Response

## Slide 70: Determining structural response
Issues
  Static or dynamic
    depends on time scale of response compared to that of load
      impulsive (short loading duration)
      sudden (short rise time)
      quasi-static (long rise time)
  Elastic or elastic-plastic
    depends on magnitude of stresses and deformation
      yield stress limit appropriate for vessels designed to contain explosions
      maximum displacement or deformation limit appropriate for determining or preventing leaks or rupture under accident conditions

## Slide 71: Simple estimates
Strength of materials approach assuming equivalent static load
  Useful only for very slow combustion (static loads) and negligible thermal load
Theory of elasticity and analytical solutions
  static solutions for many common vessels and components (Roarke’s Handbook)
  dynamic solutions available for simple shapes – mode shapes and vibrational periods are tabulated.
  Energy methods with assumed mode shapes (Baker et al method)
  Analytical models for traveling loads available for shock and detonation waves
  Transient thermo-elastic solutions available for simple shapes
Theory of plasticity
  rigid-plastic solutions available for simple shapes and impulsive loads.
  Energy methods can provide quick bounds on deformation
Empirical correlations
  Test data available for certain shapes (clamped plates) and impulsive loads
  Pressure-impulse damage criteria have been measured for many items and people subjected to blast loading
Spring-mass system models
  single degree of freedom
  multi-degree of freedom
  elastic vs plastic spring elements

## Slide 72: Simple Structural Models
Ignore elastic wave propagation within structure
Lump mass and stiffness into discrete elements
  Mass matrix M
  Stiffness matrix K
  Displacements Xi
  Applied forces Fi
Equivalent to modeling structure as coupled “spring-mass” system
Results in a spectrum of vibrational frequencies I corresponding to different vibrational modes
  Fundamental (lowest) mode usually most relevant

## Slide 73: Single Degree of Freedom Models (SDOF)
Effective mass M
Effective stiffness K
One displacement motion X
Force = mass x acceleration
Equivalent to spring-mass system
Elastic motion is oscillation of displacement x = X-Xo with period T
T

## Slide 74: Forced Oscillation of SDOF system
Blast wave characterized by
  Peak pressure DP
  Decay time t
Forced harmonic oscillator,
F(t) = ADP(t)
Response is forced oscillation
t
Dp
t

## Slide 75: SODF - Square Pulse

## Slide 76: SDOF -Impulsive Regime
Sudden load application, short duration of loading  << T
Linear scaling between maximum strain/ displacement and impulse in elastic regime:
Impulse generates initial velocity
Energy conservation determines maximum deflection

## Slide 77: SDOF – Sudden regime
Quick application of load and long duration
u >> T
Peak deflection is twice static value for same maximum load
FMax
T
time
force
displacement

## Slide 78: SDOF – Static Regime
Very slow application of load – (quasi-static) no oscillations
T << u or L
Static deflection
FMax
T
time
force
displacement

## Slide 79: SDOF - Dynamic load factor (DLF)

## Slide 80: SDOF - Plasticity
Replace kX with nonlinear relationship based on flow stress curve ()
Energy absorbed by plastic work is much higher than elastic work
Peak deformation for impulsive load scales with impulse squared.

## Slide 81: Example of SDOF Modeling
Radial oscillation of cylinders
Bending of beams or columns
P(t)
R
x
h
Frequencies are “lowest or fundamental mode” – these are usually the most important modes for
structural response to explosions.

## Slide 82: Modes of Beam Oscillation
Morse and Ingard – Theoretical Acoustics
Notes: From Morse and Ingard

## Slide 83: Pressure-Impulse (P-I) Structure Response
More realistic representation of response
For fixed Xmax and pulse shape, unique relation between peak pressure (P) and impulse (I)
Shock wave with
exponential tail
Limiting cases:
Short pulse – impulse determines damage
Long pulse – peak pressure determines

## Slide 84: P-I Damage thresholds II
From Baker et al.
Brick structures (WWII)

## Slide 85: P-I Damage Thresholds II
Ear drums

## Slide 86: Example
Blast wave from 50 lbs TNT equivalent at 100 ft range
Use charts or correlations from Dorofeev
E = 4.52x50/2.2 = 103 MJ Rs = (1 x 108 / 105 )1/3 = 10 m or 33 ft
R* = 30.5/10 = 3 P* = 0.085 or DP = 1.25 psi (8.5 kPa)
I* = 0.012 T = 3/340 = 8.8 ms I = 10 Pa s
These are “side-on” parameters, normal reflection will approximately double
overpressure and impulse in this regime.

## Slide 87: P-I Results
Brick structures
Ear drums
Your ears will be ringing but the building is undamaged!

## Slide 88: Numerical simulation
Finite element models
    static
    vibration: mode shape and frequencies
    dynamic
      transient response to specified loading
      elastic
      plastic/fracture
Numerical integration of simple models with complex loading histories
  spring-mass systems
  Elasticity with assumed mode shape

## Slide 89: Blast Loading Dynamic Response
Example: Cantilever Beam

## Slide 90: Blast Incident on a Cantilever Beam
Blast loading of a cantilever beam
Forces
  Initial impulse of shock
  Flow and drag
Elastic response
  Giordona et al
plastic response
  Van Netton and Dewey

## Slide 91: Forces on Blast-loaded Cantilever
Van Netten and Dewey, Shock Waves (1997) 7: 175–190
Shock wave interaction
  Sudden load to arrival of shock and propagation around cylinder
  Usually impulsive
Following flow
  Continuous load due to separated flow around cylinder.
  Transient drag loading

## Slide 92: Force due to flow induced by blast wave
Van Netten and Dewey, Shock Waves (1997) 7: 175–190

## Slide 93: Initial stages of shock diffraction over a cantilever beam
Giordano et al, Shock Waves 14 (1-2), 103-110, 2005.
Immediately after the shock wave passes over the beam there is no deflection.
Purely elastic case.
Experiment (left)
Computation (right)

## Slide 94: Later stages of diffraction over a cantilever beam
Giordano et al, Shock Waves 14 (1-2), 103-110, 2005.
After some time, the beam starts to deform. Dynamic response of beam and inertia are important physical effects.
Purely elastic case.
Experiment (left)
Computation (right)

## Slide 95: Applied Load and Oscillations of Beam
Giordano et al, Shock Waves 14 (1-2), 103-110, 2005.
Note the harmonic motion of the
beam after incident and reflected shock.

## Slide 96: Plastic Deformation of Blast loaded Cantilever
Van Netten and Dewey, Shock Waves (1997) 7: 175–190
Permanent deformation of beam due to formation of a “plastic hinge” at the base. Stresses exceed the yield strength of the material and beam remains permanently bent over. Deflection depends on loading history.
Can be used as a “blast gage” for ideal explosives.

## Slide 97: Shock tube experiments
Van Netten and Dewey, Shock Waves (1997) 7: 175–190
Deformation of a 200 mm long, 1.55 mm dia aluminum rod due to a M = 1.23 shock, 1 ms intervals
Final angle of deformation for 50 mm
long, 1 mm dia solder rods.

## Slide 98: Internal Explosions
Deflagrations and Detonations in Vessels

## Slide 99: Creation of flow by Explosions I.
Flames create flow due to expansion of products pushing against confining surfaces
Consider ignition at the closed-end of a tube
  Expansion ratio
  Flame velocity
  Flow velocity
Burned (u =0)
Vf
Unburned u > 0
flame
ST
Blast wave
u = 0

## Slide 100: Creation of flow by Explosions II
Detonations and shock waves create flow due to acceleration by pressure gradients in waves
Consider ignition of detonation at the closed-end of a tube
Burned (u =0)
Burned u >0
Unburned u = 0
Detonation
wave
Expansion wave
u
x
Ideal (Taylor-Zeldovich)
Adiabatic & frictionless
closed

## Slide 101: Internal Explosion - Deflagration
Limiting pressure determined by thermodynamic considerations
  Adiabatic combustion process
  Chemical equilibrium in products
  Constant volume
Initial pressure-time history determined by flame speed
fuel-air mixture
Products
Combustion wave
Vf = Sf + u
Vf
Sf
u

## Slide 102: Laminar Flame Propagation

## Slide 103: Breakdown of Initially Laminar Flame
Mixture of H2-propane that simulates Jet A
spark

## Slide 104: Flame growth and pressure rise

## Slide 105: Pressure in Closed Vessel Explosion
Peak pressure limited by heat transfer during burn and any
Venting that takes place due to openings or structural failure
Notes: O Kunz Combustion characteristics of hydrogen- and hydrocarbon-air mixtures in closed vessels. Technical Report FM98-4, GALCIT, March 1998.

## Slide 106: Burning Velocity
Laminar burning speed depends on substance, composition, pressure, temperature
Flames in explosions are turbulent, effective burning speed much higher
Notes: O Kunz Combustion characteristics of hydrogen- and hydrocarbon-air mixtures in closed vessels. Technical Report FM98-4, GALCIT, March 1998.

## Slide 107: Adiabatic Explosion Pressure
Pressure of products if there are no heat losses and complete reaction occurs
Energy balance at constant volume
Ereactants(Treactants) = Eproducts(Tproducts)
Vreactants = Vproducts
Pp = Pr (NpTp/NrTr)
Products in thermodynamic equilibrium
For stoichiometric HC fuel-air mixtures: Pp ~ 8-10 Pr
Decreases for off-stoichiometric, and diluted mixtures,
Values are similar for all HC fuels when expressed in terms of equivalence ratio.
Upper bound for peak pressure as long as no significant flame acceleration occurs

## Slide 108: Measured Peak Pressure vs Calculated
Notes: O Kunz Combustion characteristics of hydrogen- and hydrocarbon-air mixtures in closed vessels. Technical Report FM98-4, GALCIT, March 1998.

## Slide 109: Structural Response to Deflagration
Quasi-static pressurization
  Spatially uniform
Structure response can be easily bounded with
  Thermochemical computations
  Static structural analysis
    Internal pressure
    Thermal stress

## Slide 110: Thermal Stress from Deflagrations
Downstream 0.6 m of tube was insulated on the inside with 6 mm of neoprene.
End-flange
Neoprene
insulation
6mm
Ignition
insulation
S0
S1
S2
S3
S4

## Slide 111: Thermal stress component of strain
Characteristic rise time of 50 ms
Contribution to hoop strain is about 125% of peak value due to mechanical loading alone.
Dominates long-time (> 100-200 ms) observations

## Slide 112: Structural failure due to deflagration
Aviation kerosene (Jet A) at 40 C, pressure of .58 bar (14 kft pressure altitude)
Notes: Movies taken by Applied Research Associates, Littleton CO as part of NTSB TWA800 Investigation.
See J. E. Shepherd, J. C. Krok, J. J. Lee, L. L. Brown, R. T. Lynch, T. M. Samaras, and M. M. Birky. Results of 1/4-scale experiments, vapor simulant and liquid Jet A tests. Explosion Dynamics Laboratory Report FM98-6, California Institute of Technology, July 1998.
Why is flammability a problem?
Well-known hazard in aviation
  Prompted switch to low vapor pressure fuels Jet A (1960s), JP-8 (1990s), JP-5 (1970s)
  Combat aircraft use active fire suppression (Halons), self-sealing tanks, rigid and flexible foams, inerting (OBIGGS) sytems.
Previously considered an acceptable risk for commerical aviation, design philosophy was to minimize ignition sources.
FAA philosophy changed after PAL/TWA 800/Thai air accidents

## Slide 113: Detonations in Piping
Accidental explosions
Potential hazard in
  Chemical processing plants
  Nuclear facilities
    Waste processing
    Fuel and waste storage
    Power plants
Test facilities
  Detonation tubes used in laboratory facilities
  Field test installations (vapor recovery systems)

## Slide 114: Recent Accidental Detonations in NPP
Hamaoka-1 NPP
Brunsbuettel KBB
Both due to generation of H2+1/2O2 by radiolysis and accumulation in
stagnant pipe legs without high-point vents or off-gas systems.

## Slide 115: Explosion Scenario
“bubble” of explosive gas (H2-N2O)
Plug of waste material
ignition
L
Motion of piping
Explosion wave propagation
Radial motion of pipe wall

## Slide 116
Bubble
Propagating
detonation
Reflected
detonation
Deflagration-to-Detonation
Transition followed by
reflection (DDT/Pressure Piling)

## Slide 117: Example of Bubble Explosion
Hoop strain [Pa]
Tube axis
Displacement
factor: 2000
L=1.24 m
D=127 mm
t=13 mm
P

## Slide 118: H2-N2O Explosion Pressure Estimates
0
10
20
30
40
50
60
70
0.0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
0.8
0.9
1.0
H
2
(molar fraction)
P/P
0
Reflected CJ
Detonation
CJ Detonation
Plateau Pressure (P
3
)
CV Explosion

## Slide 119: Radial (Hoop) motion of Pipes: SDOF Model
Allow only for radial displacement x of tube surface
Assumes radial and axial symmetry of load
Stress in hoop direction is restoring force
P(t)
x
Results in harmonic oscillator equation (no damping)
t
reduced
frequency
R
reduced
driving force
for tube

## Slide 120: Dynamic Loading Factor
Sudden
Quasi-static
Impulsive

## Slide 121: Effect of load localization
p
w
Infinite thin-walled (R/t>10) cylinder of radius R under uniform radial pressure p over length w.
2R
t

## Slide 122: Load Length Factor

## Slide 123: BOC Methodology
Estimate loading using SDOF model and account for finite length of load.
From explosion pressure
estimate
Diameter and Schedule of pipe
Dynamic Load Factor
Load length factor
Yield stress

## Slide 124: Hazard larger for bigger, thinner pipes
0
1
2
3
4
5
6
0
10
20
30
40
50
Radius/thickness
Max initial pressure (bar)
Schedule 10
Schedule 40
Schedule 80
Schedule 160
WT1
WT2
WT3
.
2-in schedule 40
10-in schedule 40
0.2% strain limit for reflected detonation pressure in H2-N2O

## Slide 125: Detonations

## Slide 126: Detonations are pressure waves
Austin & Shepherd 2003

## Slide 127: Detonation Followed by an Expansion Wave
closed end
L
x
particle path
t
0
open end
2
1 - at rest
3
detonation
expansion fan
Stationary region
“Taylor-Zel’dovich” wave – similarity solution for constant detonation speed and
Isentropic flow in perfect gas.

## Slide 128: Spatial distribution of Pressure
Spreads linearly with increasing time.

## Slide 129: What is actual situation?
Real gases
  Viscous flow
  Heat conduction
  Turbulence (Re > 106)
Expansion flow reaches fixed duration
  L/D > 100-200 => finite length of expansion wave
  Impulse behind wave stops growing with increased length
Heat and momentum transfer to tube
  Alters velocity profile
  Drops temperature and pressure

## Slide 130: Experimental Results and Quasi-1D Models
L/d = 550, H2+1/2O2 Edwards et al 1970, Hanson and Radulescu 2005

## Slide 131: Ideal Model good for Short Tubes
L/d = 50, C3H8+5O2 Harris et al 2001, Hanson and Radulescu 2005
L/d = 18, H2+Air, Hanson and Radulescu 2005

## Slide 132: Heat and Momentum Transfer – Real Flows
Effect of tube size
Boundary layer - thermal and momentum

## Slide 133: Detonations Excite Flexural Waves in Piping

## Slide 134: Measuring Elastic Vibration
Chao 2004
Strain gage
Optical Vibrometer

## Slide 135: Flexural Wave Resonance in Tubes
Coupled response due to hoop oscillations and bending
Traveling load can excite resonance when flexural wave group velocity matches wave speed
Can be treated with analytical and FEM models
Chart: 
Measured strain (hoop)
t (ms)
0
2
4
6
8
10-4
Amplification factor
U (m/s)
Beltman and Shepherd 2002

## Slide 136: Detonation-Induced Failure of Piping Systems
Initiation of cracks at flaws
Plastic deformation at
  Location of transition from deflagration to detonation
  Reflection from bends, tees, dead ends
Rupture
  Plastic instability to to prolonged application of high pressure
Bending pipes or support structures
  Forces created by detonation wave changing direction

## Slide 137: Detonation-Induced Fracture
Fracture
External Blast
Chao 2004

## Slide 138: Post-test Al 6061-T6 Specimens (Pcj = 6.2 MPa)
Surface Notch Length = 1.27 cm
Outer diameter: 41.28 mm, Wall thickness: 0.89 mm, Length: 0.914 m
Surface notch dimensions: Width: 0.25 mm, Notch depth: 0.56 mm
Chao 2004
Detonation wave direction
Surface Notch Length = 2.54 cm
Surface Notch Length = 5.08 cm
Surface Notch Length = 7.62 cm
Fracture Behavior is a Strong Function of Initial Flaw Length

## Slide 139: Special Issues in Piping Systems
Two types of loads :
  Short period hoop oscillation
  Long period beam bending modes
Significant in piping systems
  Traveling load creates series of impulses at bends, tees and closed ends
  Dynamic pressure must be accounted for in computing magnitude of impulse
  Strains due to bending comparable or larger than hoop strains

## Slide 140: Piping System Response
Straight pipe
bend
tee
closed end

## Slide 141: Simulation (R. Dieterding ORNL)

## Slide 142: Pressure Waves on 90o Bend
Liang, Curran and Shepherd 2007

## Slide 143: Transverse Flow Forces in a 90o Bend
Momentum equation (general case):
Simplification for uniform, steady flow:
General unsteady case:
Behind detonation front
Dynamic pressure within Taylor wave
Approximate transverse force
Shepherd and Akbar 2009 FM2008.002

## Slide 146
F = 1 Reflected CJ
F = 1 Propagating CJ

## Slide 147: Control Volume Bend Force Model

## Slide 148: Measuring Axial Strains

## Slide 149: Bend Force Estimation for CJ Detonation

## Slide 150: Axial Strain Pulses – Measured vs Predicted

## Slide 151
Direct Force Measurement
Beam
Pipe

## Slide 152: Deflagration-to-Detonation Transition (DDT)

## Slide 153: DDT
Deflagration to detonation transition is a common industrial hazard with gaseous explosions
Compression of gas by flame increases pressure when detonation finally occurs “pressure piling”.
Represents upper bound in severity of pressure loading.

## Slide 154: Deflagration to Detonation Transition
burned
unburned
1. A smooth flame with laminar flow ahead
2. First wrinkling of flame and instability of upstream flow
3. Breakdown into turbulent flow and a corrugated flame
4. Production of pressure waves ahead of turbulent flame
5. Local explosion of vortical structure within the flame
6. Transition to detonation
Flame creates flow
  Pressure build-up
Detonation onset
  Localized

## Slide 155: DDT Near End Flange
15% H2 in H2-N2O at 1 atm initial pressure
Thermal ignition
Tab obstacles inside 5’ long tube
Strain (microstrain)
Pressure History
Strain History

## Slide 158: DDT Structural Loading CIT ES1 Testing
DDT at End

## Slide 159: Other DDT Testing
Thick walled vessels for elastic response
Thin-walled vessels for plastic response and failure
Use bars or tabs as “obstacles” to cause flame acceleration
Range of mixtures studied H2-N2O, H2-O2, CH4, C2H4, C3H8-O2
Measurement of strain and pressure

## Slide 160: DDT Near End Flange
15% H2 in H2-N2O at 1 atm initial pressure
Thermal ignition
Tab obstacles inside tube
Strain (microstrain)
Liang, Karnesky & Shepherd 2006

## Slide 161: H2-O2
CJ- ref
CJ
CV
Pintgen, Liang, & Shepherd 2007

## Slide 162: CH4-O2
Pintgen, Liang, & Shepherd 2007

## Slide 163: Conclusions of DDT Testing
Peak pressures in DDT up to 10 X CJ-ref
  White 1957, Kogarko 1958, Craven and Grieg 1967, etc.
Load is in impulsive regime
Peak strain is comparable to 2.5 x static strain of reflected detonation
Results for four fuel-oxygen systems comparable (H2, CH4, C2H4, C3H8)

## Slide 164: Water-Hammer Induced by Detonation

## Slide 165: Elementary Theory
165
165
Elastic tension precursor
sound speed in water
Flexural wave in tube coupled to water compression wave
’’water hammer’’
Joukowsky 1898, von Karman 1911, Skalak 1956, Tijsseling 1996
(Al tube)
Notes: 165
Present study will extend water hammer to very nonlinear modes with plastic deformation of the confining tube rather than just elastic.

## Slide 169: Modeling Piping Response To Detonations
SDOF model for hoop oscillations
Simplified traveling wave model
  Beam on an elastic foundation
Analytical shell models
  (Tang) with rotary inertia
Numerical simulation
  Shell models (Cirak)
  FEM models (LS-Dyna)
Structural models for piping systems with bends, tees, supports, and nozzles.

## Slide 170: Reference Books

## Slide 171: References on Gaseous Explosions
W. E. Baker, P. A. Cox, P. S.Westine, J. J. Kulesz, and R. A. Strehlow. Explosion Hazards and Evaluation. Elsevier, 1983. This is the classic monograph with an extensive discussion of all aspects of explosion and structural response. It is intended to be a detailed technical reference and guide for engineers involved in safety assessments. The book emphasizes hand calculation methods and is approximately evenly divided between the topics of characterizing explosion loading, and models of structural response. There are chapters on fragment and thermal effects, and also a discussion on damage criteria.
Anon. Guidelines for Evaluating the Characteristics of Vapor Cloud Explosions, Flash Fires, and BLEVEs. AIChE, 1994. Center for Chemical Process Safety. This monograph is one of the series of publications by the Center for Chemical Process Safety (CCPS) of the American Institute of Chemical Engineers http://www.aiche.org/ccps/. The emphasis is on pressure wave and thermal radiation from uncon¯ned vapor clouds and boiling liquid expanding vapor explosions (BLEVE). Oriented toward chemical process plant safety.

## Slide 172: References on Gaseous Explosions (cont)
J. M. Kuchta. Investigation of ¯re and explosion accidents in chemical, mining, and fuel-related industries - a manual. Bulletin 680, Bureau of Mines, 1985. The Bureau of Mines carried out an extensive research program on gaseous explosions and this publication summarizes much of the data on °ammability and explosion phenomena obtained by this group through the mid 1980s.
Dag Bjerketvedt, Jan Roar Bakke, and Kees van Wingerden. Gas explosion handbook. Journal Of Hazardous Materials, 52(1):1{150, January 1997. See the most recent online version at http://www.gexcon.com/. The group at GEXCON AS has been very actively involved in explosion incident investigation and explosion protection studies. Their FLACS program is one of the most widely used tools for evaluating pressure wave generation by vapor cloud explosions in industrial facilities. This handbook (now online) provides a relatively easy to read introduction to all aspects of explosions with Chapter 8 providing an introduction to structural response.
K. Gugan. Unconfined Vapor Cloud Explosions. Gulf Publishing Company, 1978. Incidents of unconfined vapor cloud explosions from 1921 through 1979 are reviewed and detailed observations of structural damage are given for selected cases. Analysis is now dated but the factual material is very useful.

## Slide 173: References on Blast Waves
S. Glasstone and P. J. Dolan. The Effects of Nuclear Weapons. United States Department of Defense and Department of Energy, 3rd edition, 1977. As title indicates, the focus is on nuclear weapons. Air blasts are a significant aspect of nuclear weapons effects and provided the motivation for the large body of work carried out on blast waves during the cold war era. Glasstone provides a detailed description of blast wave phenomena and the effect of nuclear blasts on structures.
W. E. Baker. Explosions in Air. University of Texas Press, Austin, Texas, 1973. Substantially overlaps material in Engineering Design Handbook. Explosions in Air. Volume 1. US Army Materiel Command, 1974. AMCP 706-181. This is the classic monograph on blast waves and is more oriented to conventional high explosives than Glasstone.
G. F. Kinney and K. J. Graham. Explosive Shocks in Air. 2nd Ed. Springer, 1985. Covers similar topics as both Baker and Glasstone but more oriented to classroom study. Some limited discussion of structural effects.
Anon. Estimating air blast characteristics for single point explosions in air, with a guide to evaluation of atmospheric propagation and effects. Technical Report ANSI S2.20-1983 (ASA20-1983), American National Standards Institute, 1983. Discusses standardized approach for scaling air blasts from an ideal (point) explosion. Discusses long range propagation in the atmosphere and effect of various weather features. Some discussion about structural effects such as window breakage.

## Slide 174: References on Structural Response
W. E. Baker, P. A. Cox, P. S. Westine, J. J. Kulesz, and R. A. Strehlow. Explosion Hazards and Evaluation. Elsevier, 1983. This is probably still the best single reference on analytical methods of structural response to explosion.
P.D. Smith and J.G. Hetherington. Blast and Ballistic Loading of Structures. Butter-worth/Heinemann, 1994. An alternative to Baker et al., covers much of same material, much less detail so that it is easier to grasp the concepts.
M. Paz and W. Leigh. Structural Dynamics. Springer, ¯fth edition, 2004. Modern all-around text on structural response, oriented to civil engineers that are interested in earthquake response of structures. Integrates use of computer simulation (SAP2000) intothe text.
J. Biggs. Introduction to structural dynamics. McGraw-Hill, Inc., 1964. ISBN 07-005255-7. This is the classic textbook on single degree of freedom modeling.
N. Jones. Structural Impact. Cambridge University Press, 1989. ISBN 0-521-30180-7. Jones has a detailed discussion of plastic deformation which applications to both impact and impulsive pressure loading.
Anon. Structures to Resist the Effects of Accident Explosions. Departments of the Army, the Navy, and the Air Force, 1990. Design guide for concrete-reinforced structures. Very comprehensive but oriented to military installations.

## Slide 175: References on Mechanics
M. F. Ashby and D. R. H. Jones. Engineering Materials I. Butterworth Heinemann, second edition, 1996. Elementary discussion of the material properties relevant to mechanics with formulas and data that are useful for order of magnitude computations.
W. Nash. Strength of Materials. Schaum's Outlines, McGraw Hill, fourth edition, 1998. A tutorial approach to the theory of the strength of materials that concentrations on beams.
A.C. Ugural and S.K. Fenster. Advanced Strength and Applied Elasticity. Elsevier, 2nd SI edition, 1987. An all-around text of elasticity, plasticity and applications to static problems in the strength of materials.
S.P. Timoshenko and J. N. Goodier. Theory of Elasticity. McGraw-HIll Publishing Company, third edition, 1970. This is the classic text on elasticity. Emphasizes analytical solutions.
N. Noda, R.B. Hetnarski, and Y. Tanigawa. Thermal Stresses. Taylor and Francis, 2002. ISBN 1-56032-971-8. If you need to solve a problem that involves thermal stresses, this is the book to go to.
D. Broek. Elementary Engineering Fracture Mechanics. Kluwer Academic Publishers, fourth revised edition, 1991. Fracture mechanics is a key part of the modern approach to designing pressure vessels and piping.
W. Johnson and P. B. Mellor. Engineering Plasticity. Ellis Horwood Limited, 1983.
C. R. Callidine. Plasticity for Engineers. Horwood Publishing Limited, 2000.

## Slide 176: Handbooks
W. Young and R. Budynas. Roark's formulas for stress and strain. McGraw-Hill, 2002. ISBN 0-07-072542-X. Seventh Edition. Roarks is an essential compendium of solutions for static problems in elasticity. Formulas for stress and strain for many shapes, boundary conditions, and loading problems are tabulated.
R. D. Blevins. Formulas for natural frequency and mode shape. van Nostrand Reinhold Company, 1979. Blevins compilation is similar in philosophy to Roark’s but focuses on dynamic solutions, speci¯cally elastic vibrations of structures. He tabulates mode shapes and vibrational frequencies for many structural elements and boundary conditions.
A. S. Kobayashi, editor. Handbook on Experimental Mechanics. Society of Experimental Mechanics, second revised edition, 1993. If you have to perform or interpret experiments, Kobayashi's handbook is an excellent guide to various experimental methods.
J.R. Davis. Carbon and Alloy Steels. ASM international, 1996. ISBN 0-87170-557-5. Data on the most common construction material for piping and pressure vessels.
C. Moosbrugger. Atlas of stress-strain curves. Materials Park, OH : ASM international, 2002. Measured stress-strain curves for a wide range of materials.

## Slide 177: Books on Related Subjects are Useful
Earthquake engineering
  Strong ground motion excites building motion
Terminal ballistics
  Projectile impact creates stress waves and vibration
Crashworthiness
  Vehicle crash mitigation
Weapons effects
  Conventional (High explosive and FAE)
  Nuclear and nuclear simulation testing
TIP – Many recent studies on structural response to blasts have been sponsored to counter terrorism – the results are often restricted to government agencies or official use only.

## Slide 178: Web Resources
For more resources, preprints, and reports from Caltech Explosion Dynamics Lab, see
http://shepherd.caltech.edu/EDL