## Slide 1: Detonation: Initiation, Propagation and Failure
Joseph E Shepherd
Aeronautics and Mechanical Engineering California Institute of Technology Pasadena, CA 91125 USA
Purdue University October 4, 2023

## Slide 2: Today’s Talk
Focus: The seemingly “simple” situation of detonations in homogeneous, premixed gases.
What are the characteristics of “simple” detonations?
Examples
Initiation and stabilization of detonations on high-speed projectiles.
Initiation of propagating detonations by strong decaying shock waves.
Initiation and failure of detonation waves propagating through area changes.
Goal: Explain the role of unsteadiness and spatial gradients within and behind the reaction zone region in these situations.
Theme: The unifying notion is the existence of critical levels of unsteadiness and gradients in flow properties that define the boundaries between flow regimes.

## Slide 3: Preliminaries
"Research is frequently the process of moving old bones from one graveyard to another"
- J. Frank Dobie

## Slide 4: What is a Detonation Wave?
  A supersonic combustion wave characterized by a unique coupling between a shock front and a zone of chemical energy release referred to as the “reaction zone.”
Not just shock-initiated combustion!

## Slide 5: Detonations are pressure waves
Beltman and Shepherd 2002
Notes: W.M. Beltman and J.E. Shepherd. Linear elastic response of tubes to internal detonation loading. Journal of Sound and Vibration, 252(4):617-655, 2002.

## Slide 6: Detonations Are Driven by Hot Combustion Product Expansion
Fuel + Oxidizer  Products
CH4 + O2  CO2 + 2H2O
Volume expansion pushes shock wave
Shock front
expansion
u = 0
u = 0
D
Chemical reaction
u

## Slide 7
Donald Chapman
Ehrile Jouguet
1889-1905

## Slide 8
Donald Chapman
Ehrile Jouguet

## Slide 9
Donald Chapman
Ehrile Jouguet
or
Sonic flow relative to wave

## Slide 10
Yakov Zel’dovich
John von Neumann
Werner Döring
”ZND’’ 1940-43
Cold fuel/oxidizer mixture
shock
induction zone
products
Temperature
reactants
radicals
Energy release
products
Sonic
plane

## Slide 11
”ZND’’ 1940-43
P
v
1
CJ
vN

## Slide 12
”ZND’’ 1940-43
thermicity

## Slide 13
”ZND’’ 1940-43

## Slide 14
G. I. Taylor
X
particle path
t
0
2
1
3
Stationary region

## Slide 15
Bach et al 1969

## Slide 18
Erpenbeck 1964, Lee and Stewart 1990, Short, Sharpe, Kasimov, Tumin, …

## Slide 19
scale:4mm
2H2-O2-85%Ar
Po=20 kPa
C3H8-5O2-60%N2
Po=20 kPa
Austin 2003
Notes: Movies obtained by Joanna Austin in Explosion Dynamics Laboratory, Caltech PASADENA, CA.
Joanna Austin. The Role of Instability in Gaseous Detonation. PhD thesis, California Institute of Technology, Pasadena, California, June 2003.

## Slide 20
Cell width measurements
Soot foil:
l
M. Kaneshige and J.E. Shepherd. Detonation database. Technical Report FM97-8,
Graduate Aeronautical Laboratories, California Institute of Technology, July 1997
Notes: See R. Akbar, M. Kaneshige, E. Schultz, and J.E. Shepherd. Detonations in H -N O-CH -NH -O -N mixtures. Technical Report FM97-3, GALCIT, July 1997.
And
JM Austin and JE Shepherd. Detonation in hydrocarbon fuel blends. Combustion and Flame, 132(1-2):73-90, 2003.
And
  J.-P. Hébral and J. E. Shepherd. User guide for detonation cell size measurement using photoshop and matlab. Technical Report FM00-6, California Institute of Technology, December 2000. Explosion Dynamics Laboratory Report.

## Slide 21: Crucial role of chemical reaction
Kaneshige 1999

## Slide 22
Strehlow 1967 2H2+O2+7Ar
Gamezo et al 1999 E/RT = 7.4 DY/Dt = -A(1-y) exp(-E/RT)

## Slide 23
2H2+O2+12Ar
2H2+O2+17Ar
H2+N2O+1.33N2
C3H8+5O2+9N2
Austin 2003

## Slide 24: Initiation
Indirect: Sparks, heat  flames  turbulence  acceleration  localized explosions  transition from deflagration to detonation.
Direct: laser or electrical breakdown, high explosives or sensitive mixture detonation, high speed projectiles: Strong shock waves rapid initiation of combustion coupling directly to shock wave.

## Slide 25: Early Studies with Projectiles
H2-Air, 0.34 atm 2605 m/s 15 mm sphere-cylinder
H2-Air, 0.34 atm 2029 m/s 15 mm sphere-cylinder
Lehr, 1972, Acta Astronautica 17, 589-597.
Notes: From Akiko Matsuo thesis

## Slide 26: Detonations?
We expected this:
Oblique detonation
But Lehr found this:
Decaying shock wave
Why? Where are the detonations?
Shepherd 1994

## Slide 27: Quest for explanation
Projectile too slow?
  No, U > UCJ (1944 m/s)
  Solutions for wave angle b possible for wide range of flow deflection q angles
CJ
CJ
vN
vN

## Slide 28: Questing further
Projectile too small?
  Nominal reaction time is 1.6 ms compared to flow time (d/V) of 10 to 20 ms.
Ideas:
  Hypersonics: Influence of shock and associated streamline curvature on reaction rate (Hornung, JFM, 1976) causes “freezing”
  Detonation: Relative size of reaction zone thickness (or cell size) compared to projectile dimensions

## Slide 29: How to sort this out?
"The problem cannot be solved by the philosopher in his armchair, but the knowledge involved was gathered only by someone at some time soiling his hands with direct contact." Percy W. Bridgman

## Slide 30: T5 Shock Tunnel

## Slide 31
25 mm diameter nylon projectile
Vp = 2200 to 2600 m/s
2H2 + O2 + nN2, 1 < n < 3.76
C2H4 + 3O2 + mN2, m = 5
C2H2 + 2.5O2 + mN2, m = 9.4
J. Bélanger, M. Kaneshige, and J.E. Shepherd. 1995, Kaneshige 1999.

## Slide 32: 2H2 + O2 + 3.76N2
0.1 bar, 2300 m/s
0.42 bar, 2430 m/s
1.70 bar, 22680 m/s
1.0 bar, 2230 m/s

## Slide 33: Reaction zone must be very thin!
Kaneshige 1999
Why must Δ⁄𝑑 be so small?

## Slide 34: Reaction Rate Sensitivity to Temperature Changes
Temperature sensitivity measured by activation energy
Stoichiometric H2-Air, Browne et al 2005
Induction Time
Energy Pulse Time

## Slide 35: Nondimensional Figures of Merit
Browne et. al,, 2005, Liang et. al, 2006
Extended second limit
UCJ
0.8UCJ

## Slide 36: Effect of shock curvature
Shock wave
Contact surface
products
Shocked but unreacted
reactants
Separation of reaction zone from shock
2. Curved shock wave creates curved streamlines
bounding expanding stream tubes behind shock.
Consider 2-D steady flow in natural coordinates:
Along streamline, distance = function(time)
1, Decrease in results in decreasing , increasing reaction zone thickness
Kaneshige 1999, Hung 2003

## Slide 37: Curved streamlines
Equivalent to stream tube expansion
Expansion competes with energy release

## Slide 38: Consequence: critical curvature
Kaneshige 1999

## Slide 39: Initiation is a transient event
Kaneshige 1999
Hung 2003

## Slide 40: Critical Conditions
Due to competition between
  energy gain by chemical reaction, time scale
  energy loss by volume expansion, time scale
Nondimensional parameters
2
3
3.5
4
5
6
7
Stoichiometric H2-Air, Us = 1975 m/s

## Slide 41: Analytical Model
Simplest model – adiabatic explosion, one-step reaction, ideal gas
Assume high activation energy and neglect reaction
Obtain analytic solution to Critical Decay Rate model:
Ignition can only occur if
Eckett et al 2000, Shepherd 2019

## Slide 42: Initiation by Blast Waves
Eckett et al 2000

## Slide 43: Key Role of Unsteadiness
Eckett et al 2000

## Slide 44: Critical Decay Rate Model
.
Quenching td < td,c.
Eckett et al 2000
Coupling, td > td,c.

## Slide 45: Detonation Diffraction
D
UCJ
t1
t3
t4
t2
accoustic corner
disturbance
signal
diffracting
shock
P4
P1
P2
P3
P5
P6
Schultz 2000, Pintgen 2004

## Slide 46: Skews construction, Shock Waves
a
Schultz 2000
B. Skews, JFM 1967, Vol 29, 297-304 and 705-719.

## Slide 47: Skew’s Construction, CJ Detonation
Schultz 2000

## Slide 48: Skew’s Construction: ZND Detonation
Schultz 2000

## Slide 49: Diffraction Types
Super-critical
C2H4+3O2+4He 100 kPa
Near-critical
H2+0.5 O2 100 kPa
Sub-critical
H2+0.5 O270 kPa
Schultz 2000

## Slide 50: Sub-critical
schlieren
schlieren
PLIF
overlay
multiple exposure
chemiluminescence
2H2 + O2 + 3Ar,
Po = 47.5kPa
shot 157
H2 + N2O,
Po = 42.5kPa
shot 152
150mm
80mm
70mm
80mm
109mm
image
type
image
height
Pintgen 2004

## Slide 51: Critical
schlieren
schlieren
PLIF
overlay
multiple exposure
chemiluminescence
150mm
80mm
70mm
80mm
109mm
image
type
image
height
2H2 + O2 + 6.1Ar,
Po = 100kPa
shot 138
H2 + N2O,
Po = 42.5kPa
shot 145
Pintgen 2004

## Slide 52: Super-critical
schlieren
schlieren
PLIF
overlay
multiple exposure
chemiluminescence
150mm
80mm
70mm
80mm
109mm
image
type
image
height
2H2 + O2 + 6.1Ar,
Po = 100kPa
shot 137
H2 + N2O,
Po = 45kPa
shot 143
Pintgen 2004

## Slide 53: Critical Effects in Diffraction
Combination of wave curvature and unsteady effects.
Critical case dominant balance is between unsteadiness and energy release as in blast initiation
Arienti and Shepherd 2005, Arienti 2002

## Slide 54: Critical Role of Activation Energy
Detonation locally decouples and fails.
Shock-reaction coupling is maintained.
qCJ = 4.15
qCJ = 3.5
Arienti and Shepherd 2005

## Slide 55: Critical Conditions in Detonations
Observed in many situations:
  Projectile initiation, critical diameter or limiting wave curvature
  Blast wave initiation, critical initiation energy
  Detonation Diffraction, critical tube or channel width
Due to sensitivity of reaction rates to small changes in temperature – activation energy
Effect of thermodynamic state changes amplified by large activation energy
Competition between energy release by combustion and expansion of gases

## Slide 56: Acknowledgements
Students, postdocs, researchers, and collaborators past and present on detonation projects:
  Hans Hornung, Ahmed Sabet, Mike Kaneshige, Jacques Belanger, Raza Akbar, Florian Pintgen, Joanna Austin, Eric Schultz, Marcia Cooper, Scott Jackson, Chris Eckett, Marco Arienti, Patrick Hung, Shannon Kao, Rita Liang, Jason Damazo, Donner Schoeffler, Branson Davis, Mark Frederick, Carson Slabaugh, and many others.
Financial support
  Caltech, Los Alamos, DOE, ONR.

## Slide 57: References
Ahmed I. Sabet. Investigation of equilibrium and chemical kinetic behaviour of detonation waves in hydrogen-air mixtures and an evaluation of the oblique detonation wave as the combustor for a scramjet. Master's thesis, Rensselaer Polytechnic University, Troy, NY, May 1990.
J.E. Shepherd. Detonation waves and propulsion. in Combustion in High-Speed Flows, pages 373–420. Kluwer, 1994.
M.J. Kaneshige and J.E. Shepherd. Oblique detonation stabilized on a hypervelocity projectile.
In 26th Symposium (International) on Combustion, pages 3015–3022, Naples, 1996.
Hornung, H.G. “Gradients at a Curved Shock in Reacting Flow.” Shock Waves 8, no. 1 (February 1, 1998): 11–21.
Michael J. Kaneshige. Gaseous Detonation Initiation and Stabilization by Hypervelocity Projectiles.
PhD thesis, California Institute of Technology, Pasadena, California, January 1999.
C.A. Eckett, J.J. Quirk, and J.E. Shepherd. The role of unsteadiness in direct initiation of gaseous detonation. Journal of Fluid Mechanics, 421:147–183, 2000.
Eric Schultz. Detonation Diffraction Through an Abrupt Area Expansion. PhD thesis, California Institute of Technology, Pasadena, California, April 2000.

## Slide 58: References
Joanna Austin.The Role of Instability in Gaseous Detonation..PhD thesis, California Institute of Technology, Pasadena, California, June 2003.
F Pintgen, CA Eckett, JM Austin, and JE Shepherd. Direct observations of reaction zone structure in propagating detonations. Combustion and Flame, 133(3):211–229, 2003.
Patrick Hung. Algorithms for Reaction Mechanism Reduction and Numerical Simulation of Detonations Initiated by Projectiles. PhD thesis, California Institute of Technology, Pasadena, California, June 2003.
Florian Pintgen Detonation diffraction in mixtures with various degrees of instability. PhD thesis, California Institute of Technology, Pasadena, California, December 2004.
M. Arienti and J.E. Shepherd. A numerical study of detonation diffraction. J. Fluid Mech., 529:117 – 146, 2005.
F. Pintgen and J. E. Shepherd. Stereoscopic imaging of transverse detonations in diffraction. Journal of Flow Visualization and Imaging Processing, 14(1):121–142, 2007.
F Pintgen and J E Shepherd. Detonation diffraction in gases. Combustion and Flame, 156(3):665–677, 2009.
J.E. Shepherd. Ignition modeling and the critical decay rate concept. Technical Report EDL2019.002, Graduate Aeronautical Laboratories, California Institute of Technology, December 2019.

## Slide 59: Resources
Explosion Dynamics Laboratory. SDToolbox: Numerical tools for shock and detonation wave modeling. GALCIT Report FM2018.001, California Institute of Technology, Pasadena, CA, January 2020. https://shepherd.caltech.edu/EDL/PublicResources/sdt/
Caltech Explosion Dynamics Website: https://shepherd.caltech.edu/EDL/
Most of our publications available for public download from EDL website or from: https://library.caltech.edu/caltechauthors

## Slide 60: Background on Detonations
The classic reference on detonation is: Ya. B. Zel’dovich and A. S. Kompaneets. Theory of Detonation. Academic Press, NY, 1960. This is an English translation of original Russian. Out of print and in many ways out of date.
A more recent theoretical treatment is given by: W. Fickett and W. C. Davis. Detonation. University of California Press, Berkeley, CA, 1979 Now available as a Dover paperback.
The best reference on gaseous detonations is: JHS Lee, The Detonation Phenomenon, Cambridge 2008.
Zhang, F. 2012. Detonation Dynamics. Vol. 6. Shock Wave Science and Technology Reference Library.Springer Verlag. Some overlap with Lee and F&D but discusses a number of specialized topics that they do not cover.
J. E. Shepherd. Detonation in gases. In Proceedings of the Combustion Institute, volume 32, pages 83–98, 2009. My survey paper. Companion presentation is on the EDL website.
M. D. Frederick, R. M. Gejji, J. E. Shepherd, and C. D. Slabaugh. Statistical analysis of detonation wave structure. Proceedings of the Combustion Institute, 2022. The most recent work on propagating detonation wave properties.